## Slide 1
Data collection, data processing and scaling
(1) relationship of Mosflm to CCP4
(2) some thoughts on data collection
(3) simple processing with Mosflm
(4) improving data collection with Mosflm
(5) simple processing with SCALA (using ccp4i)
Harry Powell, San Antonio, May 25th 2002
Notes: The scope of this talk is to cover the relationship of Mosflm to CCP4, simple processing of oscillation images with Mosflm using the Graphical User Interface (GUI), then to show how data collection itself can be improved by use of the STRATEGY option. Following this, use of command-line controls will be demonstrated, and the differences between the two modes of running Mosflm discussed. Finally, straightforward scaling and merging with SCALA will be dealt with, via the ccp4i GUI.
Mosflm is available free of charge to the end user; it has all necessary functionality to process diffraction images obtained on a wide variety of different detectors, and runs on all common UNIX-based computers used in crystallographic laboratories. A version which will run under Windows is currently under development.
The primary source of information about the program is
http://www.mrc-lmb.cam.ac.uk/harry/mosflm
Advice can be obtained from the program’s authors;
andrew@mrc-lmb.cam.ac.uk
harry@mrc-lmb.cam.ac.uk

## Slide 2
Notes: Mosflm is distributed with the CCP4 suite; it writes its reflection data directly to an MTZ file, which is the binary data format used by CCP4 programs. The data within these files are organized so that they can be used efficiently by the programs; it is possible to view the contents of the MTZ file conveniently by using the command-line program MTZDUMP or by using the ccp4i GUI.
The ccp4i GUI is supplied with a set of “roadmaps” which are designed to help the user navigate their way around tasks using the CCP4 suite. This example also shows how to import data which has been processed with some other integration programs. The important part of this slide, however is highlighted on the right-hand side!

## Slide 3
* Number of Datasets = 1
* Dataset ID, project/crystal name, dataset name, cell dimensions, wavelength:
1 lys_fine /
02_05_02:13:53:50
78.1485 78.1485 37.0149 90.0000 90.0000 90.0000
1.54180
* Number of Columns = 16
* Number of Reflections = 13368
* Missing value set to NaN in input mtz file
* Number of Batches = 50
* HISTORY for current MTZ file :
From MOSFLM run on 2/ 5/02
<snip>
* Resolution Range :
0.00089 0.17159 ( 33.520 - 2.414 A )
* There is no sort order recorded in the MTZ header
* Space group = P43212 (number 96)
Notes: This is an edited example of the header information contained in a typical multi-record MTZ file output from Mosflm; it has been processed from a single dataset (following scaling and merging with e.g. heavy atom derivatives an MTZ file can contain multiple dataset information). By default, if no values are supplied by the user, the Project name is set to the image filename stem, and the Dataset name is set to the date (UK style!) and time of processing. The refined cell dimensions and the wavelength used in processing are also recorded, as are the total number of reflections integrated and the number of images processed. The resolution range of the reflections in the file and the space group used are also recorded. There are 16 columns of reflection in this MTZ file;
H K L indices of the reflection
M/ISYM combined flag for full/partial and symmetry operator code
BATCH which image the reflection is on
I SIGI intensity and sigma(I) (summation integration)
IPR SIGIPR profile fitted intensity and sigma(I)
FRACTIONCALC calculated fraction of the reflection on this image
XDET YDET detector coordinates (pixels)
ROT WIDTH phi centroid and angular width of the reflection
LP Lorentz and polarization factor
MPART partiality flag

## Slide 4
The X-ray Experiment
crystal
X-rays
images
integrate
scale
phase
Mosflm
SCALA
Notes: The X-ray diffraction experiment fits into the middle of this sequence (which extends beyond the top left to the protein (or other molecule) and the organism, and beyond the bottom right to building, refinement, interpretation, etc. Integration and scaling are the part of the X-ray experiment which turn the raw data from the images into a more useful form for the subsequent steps.
Mosflm integrates the images and writes the Lorentz and polarization corrected intensities to a multi-record MTZ file.
Each image in a dataset probably has its recorded intensities on a different scale for a variety of reasons, e.g. variation in intensity of the incident radiation, absorption of diffracted rays, change in the diffracting volume, etc. In the process of merging symmetry equivalent reflections from different images, we need to take this into account and apply scales accordingly. This process is performed by SCALA.

## Slide 5
Optimization of Data Collection
Pre-process at least one image (preferably two at 90º to each other) to obtain:
Cell parameters, crystal orientation and putative Laue group
Estimate of mosaicity
Effective resolution limit
Crystal to detector distance
Exposure time
Strategy for data collection
Remember! This is the last experimental stage - if you collect bad data now you are stuck with it. No data processing program can rescue the irredeemable!
Notes: It is always worthwhile spending some time prior to the full data collection to determine sensible parameters for the data collection. For example;
are you using the full area of the detector?
does useful diffraction go beyond the edge of the detector? Does it stop halfway to the edge?
check for overloads - are there a lot? Are you using the full dynamic range of the detector? Consider a low and a high-resolution pass. Increase or decrease the exposure time.
check that the predicted spots do coincide with their positions on the image(s); is your initial estimate of the mosaicity realistic?
Remember to use prior information! If you have experience of your particular sample or experimental setup, use your knowledge. If something looks odd, investigate it.

## Slide 6
What is needed prior to running Mosflm?
X-ray images
Experimental details (e.g. detector type, direct beam position, wavelength, etc)
The program itself and a computer to run it on!
Notes: Before running Mosflm, the user needs to have access to oscillation images and a copy of the program which will run on their computer. Pre-compiled binaries which will run “out-of-the-box” are available from our web- and ftp sites, and a “build-it-yourself” version is also available. Full installation details are included with the downloads.
The computer itself must be UNIX based (but a version of Mosflm which will run under Windows is under development) and have at least 32Mb RAM and 128 Mb swap space available. A screen resolution of 1280 x 1024 pixels is useful (otherwise a small-screen version can be used).
Many experimental details are written to image headers, and Mosflm can read and use this information. All values supplied in the headers can be over-ridden by the user during processing. Further, Mosflm will determine suitable processing parameters based on analysis of the images during the processing itself, e.g. integration box dimensions.

## Slide 7
[localhost:~/test/muldlx1] harry% ls *mar2000
muldlx1_301.mar2000 muldlx1_307.mar2000 muldlx1_313.mar2000 muldlx1_319.mar2000
muldlx1_302.mar2000 muldlx1_308.mar2000 muldlx1_314.mar2000 muldlx1_320.mar2000
muldlx1_303.mar2000 muldlx1_309.mar2000 muldlx1_315.mar2000 muldlx1_321.mar2000
muldlx1_304.mar2000 muldlx1_310.mar2000 muldlx1_316.mar2000 muldlx1_322.mar2000
muldlx1_305.mar2000 muldlx1_311.mar2000 muldlx1_317.mar2000
muldlx1_306.mar2000 muldlx1_312.mar2000 muldlx1_318.mar2000
[localhost:~/test/muldlx1] harry% ipmosflm
************ Version 6.2.1 for Image plate and CCD data 23 April 2002 ***********
A.G.W. Leslie, MRC Laboratory Of Molecular Biology, HILLS ROAD, CAMBRIDGE CB2 2QH, UK
E-mail andrew@mrc-lmb.cam.ac.uk
New auto-indexing using DPS due to Ingo Steller Robert Bolotovsky and Michael Rossmann
(1998) J. Appl. Cryst. 30, 1036-1040
Original auto-indexing using REFIX due to Wolfgang Kabsch (Kabsch,W. (1993),
J.Appl.Cryst. 24,795-800.)
X-windows interface using xdl_view due to John Campbell (Daresbury Laboratory, UK.)
(Campbell,J.W. (1995) J. Appl. Cryst. 28, 236-242.
MOSFLM => image muldlx1_301.mar2000
MOSFLM => go
(Q)QOPEN: file opened on unit 1 Status: READONLY
<B><FONT COLOR="#FF0000"><!--SUMMARY_BEGIN-->
Logical Name: muldlx1_301.mar2000 Filename: muldlx1_301.mar2000
<!--SUMMARY_END--></FONT></B>
Crystal to detector distance of 250.00mm taken from image header
Wavelength of 1.54180A taken from image header
Notes: To run Mosflm, you need to have the program in your path and you need to know what it’s called on your system - often it’s “ipmosflm”.
If you run Mosflm and encounter difficulties and need help, make sure that you report which version of the program you are running - this is the first line of output to the screen, and also the first line in the standard log file, usually called mosflm.lp.
In this example, using a Mar image plate, the detector type is automatically detected so no DETECTOR keyword is necessary. For other detector types (e.g. ADSC, Rigaku, DIP, Mar CCD), default values are set up by using this keyword in conjunction with the detector type.
The GO keyword in conjunction with IMAGE tells the program to use the X-windows GUI for further processing.
The header information is read; in this case the crystal to detector distance, the wavelength, the pixel size of the detector, and the oscillation range of this image.

## Slide 8
Crystal to detector distance of 250.00mm taken from image header
Wavelength of 1.54180A taken from image header
Pixel size of 0.1500mm taken from image header.
Start and end phi values for image 1 from image header are 279.00 and 280.00 degrees.
image FILENAME: muldlx1_301.mar2000
(Q)QOPEN: file opened on unit 1 Status: READONLY
<B><FONT COLOR="#FF0000"><!--SUMMARY_BEGIN-->
Logical Name: muldlx1_301.mar2000 Filename: muldlx1_301.mar2000
<!--SUMMARY_END--></FONT></B>
The red circle denotes the region behind the backstop shadow
(Use BACKSTOP keyword to set this.)
Notes: Once the header information has been read and appropriate parameters set up, the image file is opened a second time and the image data read. Following this, the X-window GUI is displayed on the screen and further processing can be performed.
Mosflm checks to see whether the image is the right size for the named detector, and also whether the data has been written on a big-endian or little-endian computer. For several detector makes, the model is also determined automatically from the image file contents.

## Slide 9
Notes: The GUI display is divided into several areas; when the mouse cursor is over any field that can be changed or is associated with an action, that field changes colour to light blue. The green box at the top left of several of the fields indicates that those parts of the display are active and ready for input.
In the “Processing params” area (on the left) clicking on a field allows the user to type in new values using the keyboard. The fields are also kept up-to-date if the parameter is updated during processing (e.g. crystal mis-setting angles).
The “Main menu” consists of buttons with actions which are reasonably self-explanatory.
The “Output” area reflects values associated with the image displayed and mouse actions on the image, e.g. start and end phi values for the image or the resolution of a pixel at the cursor position.
The image display can be modified with the controls at the top right; also included is a button to allow the current view to be saved as a PostScript file for printing.
A field at the bottom of the display gives information which may be useful at different times in the processing, and a pop-up display informs the user whether the program is processing or waiting for an input.

## Slide 10
Notes: When an action on the Main menu is performed, it is often followed by a pop-up dialogue window appearing; there is useful text here, usually with a number of questions that require answers. In most cases, a suitable default answer is given, and this will be used simply by pressing the <Return> key.
In the case shown, the “Find spots” button has been pressed. The information here is most useful if autoindexing has failed on a previous run, as it gives suggestions as to the parameters which can be changed to improve the spot list.
Note also the rectangular red box which appears on the image; this is used to determine the radial background, used in discriminating spots from background at different detector radii.
The following image has been indexed and its mosaicity estimated. The predicted spot positions have been displayed and categorized (blue = fulls, yellow = partials, red = overlaps and green = too wide in phi (i.e. they cannot completely traverse the Ewald sphere with this cell and mosaicity) .

## Slide 11
Notes: A minimal sequence of commands to process a dataset would be as follows;
Autoindex the image (if no spots have already been found, then the program will do this first).
Estimate Mosaicity: this gives a working value for the mosaicity; it is reliable for images provided there is little thermal diffuse scattering.
Predict: overlays the predicted spot positions with boxes; always check that the cell and mosaicity found in the previous two steps match the image!
Beam/backstop: use this to eliminate the area in the backstop shadow from integration.
Integrate: run an integration on a single image to check on the effective resolution of the data.
Refine cell: get the best possible fit of calculated to observed spot positions before integrating.
It is normal at this point in the process to close down the GUI and complete processing from the command line or from a command file because these routes are much faster than using the GUI. Mosflm prompts the user to save the current parameters in a file, which can be used in a separate run of Mosflm.
Integrate: integrate the whole dataset.

## Slide 12
Notes: The first step in processing any dataset is to index the images, usually by autoindexing. Mosflm has two autoindexing routines available; the new-style routine uses FFTs, and is used by default as it is very reliable. The indexing can be performed with spots obtained on either a single image or from several.
Fixing the detector distance for this stage is highly recommended. The program prompts for a filename for storing the final orientation matrix (which can be read using the command “MATRIX <filename>”; a maximum likely cell edge is required by the FFT indexing, but the program makes an estimate based on the inter-spot separation, the crystal to detector distance and the wavelength of radiation. Pre-refining before choosing a solution can be helpful in discriminating good high symmetry solutions. The penalties are based on the goodness-of-fit of the 44 lattice characters to the primitive triclinic solution, and are normalised to give a maximum penalty of 999.
Solutions with a penalty less than 200 are presented in a new pop-up window. As a rule of thumb, if nothing is known about the crystal, choose an initial solution in this way;
note where there is a sharp drop in the penalty - in this case, after solution #10.
pick the solution with the highest symmetry with a penalty lower than the sharp drop - in this case, solution #10, which is either trigonal or hexagonal. The list of space groups is simply a reminder of the possible choice available;

## Slide 13
Notes: no systematic absences other than those from the Bravais lattice are excluded in processing (e.g. all those absences due to screw axes are included in the results).
It should be stressed at this stage that the penalties are calculated only on the metric symmetry of the cell; it is perfectly possible (and indeed relatively common!) to have a monoclinic cell with  ≈ 90.00º (and thus appear to be orthorhombic), or an orthorhombic cell with a ≈ b (and appear to be tetragonal). It is only possible to be reasonably certain about the true crystal symmetry after merging equivalents and examining the statistics.
Tell Mosflm which solution you have chosen by typing the solution number and space group - prior knowledge has been applied here as the crystal is known to be P64.
Mosflm then refines the solution and applies suitable symmetry - here, forcing a = b, and  =  = 90º,  = 120º. The final SD in spot positions for good spots on an accurately aligned detector should be ~0.5 - 1.0x the pixel size (0.15mm for Mar IP), and around 0.25 - 0.5x the oscillation angle (in this case 1.0º).
The main beam position is refined simultaneously; it should not change by more than a few pixels, and in any case should be known to within 0.5x the minimum spot separation for the expected unit cell, wavelength and distance. Shifts larger than this are commented on in the output!
At each stage the user has the choice of accepting or rejecting the Mosflm’s suggestion. Usually, it is best to accept unless there is contradictory prior knowledge.
Following the autoindexing step, estimate the mosaicity (either by eye/trial and error, or using the built-in function), and run a spot prediction. The coloured boxes should coincide with the observed spots on the image.
Autoindexing can often be improved considerably by using two images 90º apart.

## Slide 14
Notes: Mosflm uses the technique of post-refinement to determine accurate cell parameters before the full integration, so the unit cell dimensions should not be refined during integration (as is the case with some other integration programs!). Post-refinement uses the phi centroids of reflections which are spread across adjacent images to refine the cell parameters, crystal mis-setting angles and mosaic spread independently of camera parameters (e.g. crystal to detector distance, yscale and tilt and twist of the detector).
Therefore post-refinement requires at least two adjacent images (if the average mosaicity ≤ twice the oscillation angle for each image) with a sufficiently large number of completely recorded partials for good statistics. If the mosaicity is larger, then more adjacent images are needed.
For crystal systems with orthorhombic or lower symmetry, two segments of data separated by ~90º should be used.

## Slide 15
Notes: Note that the “Main menu” changes when we are running post-refinement; this also happens when we integrate with the GUI.
Clicking on the “Continue” button lets Mosflm proceed stepwise through the refinement. It’s worthwhile stepping slowly for the first few steps, but once you are satisfied things are proceeding well, click on the “Timeout mode” button (bottom left of the GUI) and Mosflm will stop “waiting for input”.
A pop-up window shows an ASCII representation of the average spot profile with figures for the RMS residual (which should be < half the pixel size) and the weighted residual (~1.0).
When post-refinement has finished, the “Main menu” changes back to the initial format.
If the detector parameters have not been defined prior to this stage, convergence can take several cycles.
Running the integration step via the GUI is done in a broadly similar fashiion.

## Slide 16
Running the STRATEGY option
In the GUI, click on the STRATEGY button
On the command-line, type STRATEGY.
In either case, determining a suitable strategy for data collection once you have a cell, orientation and crystal symmetry is straightforward.
Then run TESTGEN to check for overlaps
Notes: If you have already collected the dataset then you will have, presumably, determined a suitable data collection strategy to give you the data that you need for your experiment. If you are at the data collection stage, on the other hand, it is important to collect the data in the best possible way. Mosflm has a STRATEGY option which calculates strategies for:
optimum unique completeness
optimum anomalous completeness
data with the crystal in this orientation given a previous data collection.
Options are available for dividing up the data collection into multiple segments (it may be more efficient to collect two smaller segments rather than one large one) and changing the number of overlapped reflections allowed, among others.

## Slide 17
Notes: If the STRATEGY button is clicked, this window appears containing a command-line prompt. Just type “STRATEGY” at the prompt, then “GO”. If you want to calculate a suitable strategy for collecting the maximum available anomalous completeness (e.g. for a MAD experiment), type “STRATEGY ANOMALOUS”, “GO”
Mosflm will determine a strategy based on the current unit cell, given symmetry and orientation of the crystal. More information can be seen by typing “STATS”; the maximum oscillation angle to avoid overlaps in different phi ranges can be calculated with the TESTGEN command.

## Slide 18
Checking the output (1)
There are two useful log files;
SUMMARY; this is of most use when viewed with the CCP4 graph viewer LOGGRAPH, as it contains graphs of parameters which have varied through the data processing.
mosflm.lp; this can be very large, and contains a complete record of the experiment.
Notes: Things to check in SUMMARY
Quickly check through all the graphs to make sure that there are no sharp discontinuities, and that all the graphs vary smoothly through the data processing run. Some parameters will not change at all (e.g. cell parameters should not be refined during the integration run), while others will drift slightly.
Check carefully that YSCALE is not changing by more than 1 part in 1000. Likewise, DISTANCE should be constant for a properly centred crystal; a large random variation in either of these indicates that postrefinement was not performed correctly - the cell parameters may be wrong, and the machine parameters may be unreliable. A regular variation (following an approximate sine curve) in DISTANCE indicates that the crystal is precessing about the true axis of rotation.
Check the Residual and Weighted Residual; both should remain roughly constant, but the weighted residual should be ~1.0 for a laboratory source; values higher than this indicate an incorrect GAIN for the detector, while smaller values are common for data collected at synchrotrons.
Check the I/sig(I) graphs; is the crystal dying? Does it diffract at the highest resolution specified in processing?

## Slide 19
Notes: These are examples from loggraph of some of the plots from the SUMMARY file. The main point to draw from these is that refinement seems stable and no parameters are swinging from one value to another.
The “residual” plot in the center shows the use of the cursor in loggraph to pick out a particular value from the graph; in this instance, the RMS residual for spots on image 316 is 0.07mm (cf pixel size of 0.15mm).
The apparent drift in the missetting angles is probably due to the rotation axis not being exactly perpendicular to the X-ray beam.

## Slide 20
Notes: Things to check in mosflm.lp
Most importantly, check for occurrences of “WARNING”, “ERROR” and “SEVERE ERROR”.
“WARNING”s are there to let you know that the program has detected a parameter which is not optimal and made an effort (usually successful) to correct it; you should not worry unduly about their presence, though it might be worthwhile checking to see if you can improve the data processing by taking a more active role.
“ERROR”s occur when something has gone wrong in the processing which the program was unable to correct on its own. By and large these are problems of omission (e.g. is a file missing?) and can be avoided by taking careful note of the errors reported and taking action accordingly.
“SEVERE”, “SERIOUS” and “FATAL” “ERROR”s cause the program to terminate. You should take careful note of what has caused the error and take steps to remedy it if possible. In some cases the only course of action is to contact the program’s authors and describe the problem to them.
Having checked for those strings in mosflm.lp, look at the end of the file for a list of specific warnings about the data processing (look for the string “*** Warning messages ***”). All these messages (if any) contain advice about how to improve the data processing; take action accordingly, but bear in mind that Mosflm will probably have managed to cope well with these circumstances and reprocessing may not improve matters much.
Having checked for warnings and errors, you should now check for rejected spots; if you processed interactively using the GUI, these will have been brought to your attention during processing, and there is (probably) no need to check now.
Check the “Final rms residual” throughout mosflm.lp; for good data with low TDS on the images, expect it to be around half the pixel size (a little more for a lab source, often less for synchrotron data); this is a reasonably good indication that all parameters have been well determined and the spot positions have been predicted well.
If the rms residual becomes high, first check that the “Total number” of reflections used in postrefinement has not dropped suddenly; it should rise through the first few images of data processing before becoming more-or-less stable.
Finally, check that I/sig(I) is significant in the high resolution shells (i.e. at least unity) and that the crystal was still diffracting at the end of the experiment (i.e. in the last image).

## Slide 21
Checking the output (2)
If everything has gone right so far;
check the MTZ file; is it as you’d expect?
Notes: Things to check in the MTZ file
The main thing is to make sure that it contains the right number of batches (one for each image)? Also (especially if they have been entered via the keyboard rather than from a command file!) check that the experimental details in the MTZ file are correct - wavelength, resolution limits, space group, etc.
While it is possible to check other items in the MTZ file produced by Mosflm, it is probably more useful at this stage to wait until after running SCALA, when full statistics on the data processing will be available.

## Slide 22
Command-line processing
Most commands in the GUI are available from the command-line; e.g. for the test images, the following could be done:
# detector mar ! not necessary here!
template muldlx1_###.pck
beam 149.79 150.87
autoindex dps image 301
mosaic estimate
go
postref segment 1
process 301 303
go
postref nosegment fix all
process 301 322
go
exit
Notes: Use of the GUI allows the user to check easily how well processing is proceeding; e.g. spot predictions can be compared with the image. However, the speed of processing can be improved greatly if Mosflm is run from the command-line instead. The only procedures unavailable are those associated with visual representation, so if the user is confident about checking the quality of processing by inspection of the log files, this can be a way to improve efficiency.
All the commands can be edited into a command file which the program can then use with the “@command-file” syntax. Note, however, that Mosflm will stop processing from a command file read in this way following the completion of any “PROCESS” command, and wait for further instructions.
Another option is to use the UNIX redirection command with a command file;
[localhost:~/test/muldlx1] harry% ipmosflm < command-file
in this case all the commands in the file will be processed, provided there are no errors.

## Slide 23
Scaling with SCALA in ccp4i
Scaling and merging the data is the next step following integration. It is important because:
it attempts to put all observations on a common scale
it provides the main diagnostics of data quality and whether the data collection is satisfactory
Because of this diagnostic role, it is important that data are scaled as soon as possible after collection, or during collection, preferably while the crystal is still on the camera.
Notes: Various physical factors lead to observed intensities being on different scales. among these factors are those related to:
the incident beam and the camera
e.g. variations in beam intensity at a synchrotron, illuminated volume of the crystal, variations in rotation speed and shutter synchronisation (these latter are disastrous!).
the crystal and the diffracted beam
e.g. absorption, radiation damage
the detector
e.g. incorrect calibration, shadows from beamstop etc.
Scaling models should (if possible) parameterise the experiment so different experiments may require different models. Scales are determined by comparison of symmetry-related reflections, i.e. by adjusting scale factors to get the best internal consistency of intensities. Note that we do not know the true intensities and an internally-consistent dataset is not necessarily correct. Systematic errors will remain despite scaling.
The diagnostics will be dealt with later.

## Slide 24
Notes: Running SCALA from ccp4i is very simple, as most parameters have been given sensible default values.
It is probably worthwhile altering two of the defaults:
Change the scaling model from “On rotation axis” to “On rotation axis with secondary beam correction”; the surface plot provided with this latter option provides a useful check for strong absorption.
Change the default rotation interval from 10 to 5 degrees, particularly if you have a large unit cell with plenty of data to scale.
It is worthwhile separating the anomalous pairs if performing a MAD experiment or similar.

## Slide 25
Checking the output of SCALA
Check these files/plots:
ROGUES
Normal probability plot(s)
Surface plot
SCALA log file
loggraph output
Notes: It’s probably easiest to check through the different log files produced by SCALA with the ccp4i GUI.
The ROGUES file contains a list of the reflections which have been rejected because the symmetry equivalents differ considerably, and also those reflections with Emin too large. It is probably worthwhile trying to work out why the reflections are there! A common reason is that one equivalent is partly hidden behind the backstop arm, so has an anomalously low intensity.
The Normal Probability Plot is useful for determining if the data have a reasonable distribution of intensities; the bulk of the points should lie on the diagonal with slope = 1, for both fully recorded reflections and partials. If there is considerable thermal diffuse scattering, the “partials” graph will be well above that of the “fulls”, indicating a negative partial bias. This may be addressed by using the “TAILS” option, which makes a reasonable attempt to correct for this effect.
The Surface Plot (produced only when a secondary beam correction is applied) is useful for determining whether or not an absorption correction is necessary; large deviations from the flat graph indicate that this might be so.
The full SCALA log file, much like the mosflm.lp file, probably contains more information than will be used. Most people will be interested in Rmeas (i.e. multiplicity weighted Rmerg), completeness and resolution figures, but it’s well worthwhile spending more than a couple of minutes checking the file.

## Slide 26
Notes: In particular, check that the scale factors are similar, especially if an absorption correction has not been performed. If there are discontinuities, then BATCH scaling is appropriate, rather than SMOOTH scaling.
Use the ccp4i utility loggraph to check through the plots; look for smooth variations in the graphs. Unexpected discontinuities can mean trouble!
Some plots (e.g. those for Scales vs rotation range, and Analysis against Batch) should be both flat and smooth. Others will have a systematic variation, e.g. the analyses against resolution.
Several plots would be expected to be discontinuous, e.g. an axial reflection plot for a screw axis, or the plot of number rejected vs range.
If discontinuities are apparent where they are not expected, then it makes good sense to break the scaling into different runs; trying to merge batches of images together which are clearly not on the same scale is inviting trouble!

## Slide 27
Notes: This is the normal probability plot produced by the current dataset when the “Tails” correction has been applied (compare with that on the previous slide). The negative partial bias produced by the TDS has been corrected for and the two plots (for fulls and partials) coincide.