## Slide 1: Data Reduction Space Group Determination, Scaling and Intensity Statistics
Phil Evans Fukuoka October 2012
MRC Laboratory of Molecular Biology
Cambridge UK

## Slide 2
Intensities
from eg Mosflm, XDS etc
h k l I σ(I) etc
h k l F σ(F) I σ(I) FreeR_flag
|F|2
I
Experiment
|F|2
I
lots of effects (“errors”)
Model of experiment
Parameterise experiment
Our job is to invert the experiment: we want to infer |F| from our measurements of intensity I
Scaling and Merging
|F|

## Slide 3
Integration and data reduction can be done in an automated pipeline such as XIA2 (Graeme Winter): this goes from images to a list of hkl F ready for structure determination)
Automation works pretty well, but in difficult cases you may need finer control over the process

## Slide 4
Note that multiple files from different “sweeps” or crystals can be combined
Determine point-group
(& space group)
and consistent indexing
Intensities
from Mosflm (or XDS)
h k l I σ(I) etc
POINTLESS
Sorted Intensities in “best” space group
AIMLESS/SCALA
Scale symmetry-related intensities together
Produce statistics on data quality
Estimate |F| from I
detect twinning (intensity statistics)
Complete sphere of reflections
Generate or copy freeR flags
Scaled and averaged intensities
CTRUNCATE
UNIQUIFY etc
h k l F σ(F) I σ(I) FreeR_flag
Data flow scheme in CCP4
Intensities
from Mosflm (or XDS)
h k l I σ(I) etc
Intensities
from Mosflm (or XDS)
h k l I σ(I) etc
One or more files from integration program
One or more datasets (eg MAD)
These programs may ultimately be combined into one

## Slide 5
h k l M/ISYM BATCH I SIGI IPR SIGIPR
...
-20 12 10 258 4 13 3 7 3...
-20 12 10 258 5 304 24 322 24...
-20 12 10 258 6 1072 84 1101 84...
-20 12 10 258 7 349 27 324 27
Track one reflection through the process
Spot profile
4
5
6
7
Spot over 4 images
In MTZ file from Mosflm, ordered by image (BATCH) number
Entries spread through file
Summation
integration
Profile fit
After POINTLESS: Possibly reindexed
observation parts grouped by reduced hkl (sorted)
Symmetry-related observations
Reduced
hkl
Original
hkl
Image number
Intensities & σ(I)
Full/part+
Symmetry
number
Fraction
Detector pixel
Width
Rotation
Partial
serial
LP
Flags
3D integration eg XDS, d*trek
2D integration eg Mosflm, hkl2000

## Slide 6
Unmerged file from Pointless, multiple entries for each unique hkl (note that we need to know the point group to connect these)
Merged file, one line for each hkl
scale and merge
AIMLESS
CTRUNCATE
Merged file, one line for each hkl, intensities and amplitudes F
Optional unmerged output
Partials summed, scaled, outliers rejected
Infer |F| from I
Full
Partial
Partial
Three symmetry-related observations for one reflection

## Slide 7
Determination of Space group
The space group symmetry is only a hypothesis until the structure is solved, since it is hard to distinguish between true crystallographic and approximate (non-crystallographic) symmetry.
By examining the symmetry of the diffraction pattern we can get a good idea of the likely space group
It is also useful to find the likely symmetry as early as possible, since this affects the data collection strategy
Stage 1: lattice symmetry
From the unit cell dimensions we can deduce the maximum possible lattice symmetry, ie the crystal system: this the only information available to the integration program (Mosflm)
Systems are :
cubic, hexagonal/trigonal, tetragonal, orthorhombic, monoclinic, or triclinic,
+ lattice centring P, C, I, R, or F
For example if a = b = c and α=β=γ=90° (within some tolerance eg 2°) then the maximum lattice symmetry is cubic

## Slide 8
Stage 2: individual rotational symmetry operators
Ignore symmetry from integration program
Test all rotation operators consistent with the lattice symmetry
Score agreement between reflections related by each operator, by R-factor (Rmeas) and correlation coefficient (CC) on normalised intensities |E|2
Calculate a “probability” based on the CC
Only orthorhombic symmetry operators are present
Analysing rotational symmetry in lattice group P m -3 m----------------------------------------------Scores for each symmetry elementNelmt Lklhd Z-cc CC N Rmeas Symmetry & operator (in Lattice Cell) 1 0.955 9.70 0.97 13557 0.073 identity 2 0.062 2.66 0.27 12829 0.488 2-fold ( 1 0 1) {+l,-k,+h} 3 0.065 2.85 0.29 10503 0.474 2-fold ( 1 0-1) {-l,-k,-h} 4 0.056 0.06 0.01 16391 0.736 2-fold ( 0 1-1) {-h,-l,-k} 5 0.057 0.05 0.00 17291 0.738 2-fold ( 0 1 1) {-h,+l,+k} 6 0.049 0.55 0.06 13758 0.692 2-fold ( 1-1 0) {-k,-h,-l} 7 0.950 9.59 0.96 12584 0.100 *** 2-fold k ( 0 1 0) {-h,+k,-l} 8 0.049 0.57 0.06 11912 0.695 2-fold ( 1 1 0) {+k,+h,-l} 9 0.948 9.57 0.96 16928 0.136 *** 2-fold h ( 1 0 0) {+h,-k,-l} 10 0.944 9.50 0.95 12884 0.161 *** 2-fold l ( 0 0 1) {-h,-k,+l} 11 0.054 0.15 0.01 23843 0.812 3-fold ( 1 1 1) {+l,+h,+k} {+k,+l,+h} 12 0.055 0.11 0.01 24859 0.825 3-fold ( 1-1-1) {-l,-h,+k} {-k,+l,-h} 13 0.055 0.14 0.01 22467 0.788 3-fold ( 1-1 1) {+l,-h,-k} {-k,-l,+h} 14 0.055 0.12 0.01 27122 0.817 3-fold ( 1 1-1) {-l,+h,-k} {+k,-l,-h} 15 0.061 -0.10 -0.01 25905 0.726 4-fold h ( 1 0 0) {+h,-l,+k} {+h,+l,-k} 16 0.060 2.53 0.25 23689 0.449 4-fold k ( 0 1 0) {+l,+k,-h} {-l,+k,+h} 17 0.049 0.56 0.06 25549 0.653 4-fold l ( 0 0 1) {-k,+h,+l} {+k,-h,+l}
Cell: 79.15 81.33 81.15 90.00 90.00 90.00 a ≈ b ≈ c
Pseudo-cubic example

## Slide 9
CC = 0.94
CC = 0.06
Linear correlation coefficient
For equal axes, the correlation coefficient (CC) is the slope of the “best” (least-squares) straight line through the scatter plot
CCs have the advantage over eg R-factors in being relatively insensitive to incorrect scales
... but they are more sensitive to outliers
... and CCs need to correlate values that come from the same distribution, ie in this case |E|2 rather than I
What score to use?

## Slide 10
Stage 3: point group
All possible combinations of rotations are scored to determine the point group.
Laue Group Lklhd NetZc Zc+ Zc- CC CC- Rmeas R- Delta ReindexOperator= 1 C m m m *** 0.989 9.45 9.62 0.17 0.96 0.02 0.08 0.76 0.0 [h,k,l] 2 P 1 2/m 1 0.004 7.22 9.68 2.46 0.97 0.25 0.06 0.56 0.0 [-1/2h+1/2k,-l,-1/2h-1/2k] 3 C 1 2/m 1 0.003 7.11 9.61 2.50 0.96 0.25 0.08 0.55 0.0 [h,k,l] 4 C 1 2/m 1 0.003 7.11 9.61 2.50 0.96 0.25 0.08 0.55 0.0 [-k,-h,-l] 5 P -1 0.000 6.40 9.67 3.27 0.97 0.33 0.06 0.49 0.0 [1/2h+1/2k,1/2h-1/2k,-l] 6 C m m m 0.000 1.91 5.11 3.20 0.51 0.32 0.34 0.51 2.5 [1/2h-1/2k,-3/2h-1/2k,-l] 7 P 6/m 0.000 1.16 4.59 3.43 0.46 0.34 0.41 0.46 2.5 [-1/2h-1/2k,-1/2h+1/2k,-l] 8 C 1 2/m 1 0.000 1.51 5.15 3.64 0.52 0.36 0.33 0.47 2.5 [1/2h-1/2k,-3/2h-1/2k,-l] 9 C 1 2/m 1 0.000 1.51 5.15 3.64 0.51 0.36 0.33 0.47 2.5 [-3/2h-1/2k,-1/2h+1/2k,-l] 10 P -3 0.000 1.04 4.75 3.71 0.48 0.37 0.40 0.45 2.5 [-1/2h-1/2k,-1/2h+1/2k,-l] 11 C m m m 0.000 2.13 5.23 3.10 0.52 0.31 0.32 0.52 2.5 [-1/2h-1/2k,-3/2h+1/2k,-l] 12 C 1 2/m 1 0.000 1.64 5.25 3.61 0.53 0.36 0.32 0.47 2.5 [-1/2h-1/2k,-3/2h+1/2k,-l] 13 C 1 2/m 1 0.000 1.67 5.27 3.60 0.53 0.36 0.32 0.47 2.5 [-3/2h+1/2k,1/2h+1/2k,-l] 14 P -3 1 m 0.000 0.12 4.00 3.87 0.40 0.39 0.44 0.44 2.5 [-1/2h-1/2k,-1/2h+1/2k,-l] 15 P -3 m 1 0.000 0.14 4.00 3.86 0.40 0.39 0.44 0.44 2.5 [-1/2h-1/2k,-1/2h+1/2k,-l] 16 P 6/m m m 0.000 3.93 3.93 0.00 0.39 0.00 0.44 0.00 2.5 [-1/2h-1/2k,-1/2h+1/2k,-l]
Good scores in symmetry operations which are absent in the sub-group count against that group.
Example: C-centred orthorhombic which might been hexagonal

## Slide 11
Analysing rotational symmetry in lattice group P 6/m m m----------------------------------------------Scores for each symmetry elementNelmt Lklhd Z-cc CC N Rmeas Symmetry & operator (in Lattice Cell) 1 0.932 9.94 0.99 1299 0.033 identity 2 0.794 8.19 0.82 1328 0.168 ** 2-fold l ( 0 0 1) {-h,-k,l} 3 0.815 8.29 0.83 1346 0.168 ** 2-fold k ( 0 1 0) {-h,h+k,-l} 4 0.625 7.55 0.76 1340 0.171 * 2-fold h ( 1 0 0) {h+k,-k,-l} 5 0.653 7.65 0.77 1362 0.173 * 2-fold ( 1-1 0) {-k,-h,-l} 6 0.934 9.83 0.98 1510 0.048 *** 2-fold ( 2-1 0) {h,-h-k,-l} 7 0.934 9.85 0.99 1486 0.045 *** 2-fold (-1 2 0) {-h-k,k,-l} 8 0.936 9.72 0.97 1450 0.055 *** 2-fold ( 1 1 0) {k,h,-l} 9 0.936 9.66 0.97 3007 0.065 *** 3-fold l ( 0 0 1) {k,-h-k,l}{-h-k,h,l} 10 0.503 7.09 0.71 2790 0.186 * 6-fold l ( 0 0 1) {h+k,-h,l}{-k,h+k,l}
What can go wrong? A bad case
Pseudo-symmetry or twinning (often connected) can suggest a point group symmetry which is too high
Careful examination of the scores for individual symmetry operators may indicate the truth (the program is not foolproof!)
Correct operators indicated for 321 point group
Twinning not detected by L-test though probably present

## Slide 12
What can go wrong?
Pseudo-symmetry or twinning (often connected) can suggest a point group symmetry which is too high
Careful examination of the scores for individual symmetry operators may indicate the truth (the program is not foolproof!)
... but POINTLESS selects the wrong Laue group in this case
Laue Group Lklhd NetZc Zc+ Zc- CC CC- Rmeas R- Delta ReindexOperator= 1 P 6/m m m *** 0.981 8.74 8.74 0.00 0.87 0.00 0.11 0.00 0.0 [h,k,l] 2 P -3 m 1 0.018 2.10 9.80 7.70 0.98 0.77 0.05 0.17 0.0 [h,k,l] 3 C m m m 0.000 0.60 9.10 8.50 0.91 0.85 0.10 0.11 0.0 [h,h+2k,l] 4 P -3 1 m 0.000 -0.12 8.68 8.80 0.87 0.88 0.11 0.10 0.0 [h,k,l] 5 C m m m 0.000 0.29 8.92 8.62 0.89 0.86 0.10 0.11 0.0 [h+k,-h+k,l] 6 C m m m 0.000 0.33 8.94 8.61 0.89 0.86 0.10 0.11 0.0 [-k,2h+k,l] 7 P 6/m 0.000 -0.09 8.69 8.78 0.87 0.88 0.11 0.11 0.0 [h,k,l] 8 P -3 0.000 1.38 9.81 8.43 0.98 0.84 0.05 0.13 0.0 [h,k,l] 9 C 1 2/m 1 0.000 1.39 9.84 8.45 0.98 0.84 0.04 0.13 0.0 [h-k,h+k,l] 10 C 1 2/m 1 0.000 1.45 9.89 8.44 0.99 0.84 0.04 0.13 0.0 [h+2k,-h,l] 11 C 1 2/m 1 0.000 1.48 9.90 8.43 0.99 0.84 0.04 0.13 0.0 [2h+k,k,l] 12 C 1 2/m 1 0.000 0.60 9.21 8.61 0.92 0.86 0.09 0.11 0.0 [h,h+2k,l] 13 P 1 2/m 1 0.000 0.55 9.17 8.62 0.92 0.86 0.09 0.11 0.0 [k,l,h] 14 C 1 2/m 1 0.000 0.20 8.90 8.70 0.89 0.87 0.09 0.11 0.0 [h+k,-h+k,l] 15 C 1 2/m 1 0.000 0.16 8.86 8.70 0.89 0.87 0.09 0.11 0.0 [-k,2h+k,l] 16 P -1 0.000 1.37 9.94 8.58 0.99 0.86 0.03 0.12 0.0 [l,-h,-k]

## Slide 13
Clear 21 axis along b
Clear 21 axis along c
Possible 21 axis along a
There are indications of 21 screw symmetry along all principle axes
(though note there are only 3 observations on the a axis (h00 reflections))
Fourier analysis of I/σ(I)
Stage 4: space group from axial systematic absences
... BUT “confidence” in space group may be low due to sparse or missing information
Always check the space group later in the structure solution!

## Slide 14
Note high confidence in Laue group, but lower confidence in space group

## Slide 15
Cell: 79.15 81.33 81.15 90.00 90.00 90.00 a ≈ b ≈ c
Pseudo-cubic example
Only orthorhombic symmetry operators are present
Analysing rotational symmetry in lattice group P m -3 m----------------------------------------------Scores for each symmetry elementNelmt Lklhd Z-cc CC N Rmeas Symmetry & operator (in Lattice Cell) 1 0.955 9.70 0.97 13557 0.073 identity 2 0.062 2.66 0.27 12829 0.488 2-fold ( 1 0 1) {+l,-k,+h} 3 0.065 2.85 0.29 10503 0.474 2-fold ( 1 0-1) {-l,-k,-h} 4 0.056 0.06 0.01 16391 0.736 2-fold ( 0 1-1) {-h,-l,-k} 5 0.057 0.05 0.00 17291 0.738 2-fold ( 0 1 1) {-h,+l,+k} 6 0.049 0.55 0.06 13758 0.692 2-fold ( 1-1 0) {-k,-h,-l} 7 0.950 9.59 0.96 12584 0.100 *** 2-fold k ( 0 1 0) {-h,+k,-l} 8 0.049 0.57 0.06 11912 0.695 2-fold ( 1 1 0) {+k,+h,-l} 9 0.948 9.57 0.96 16928 0.136 *** 2-fold h ( 1 0 0) {+h,-k,-l} 10 0.944 9.50 0.95 12884 0.161 *** 2-fold l ( 0 0 1) {-h,-k,+l} 11 0.054 0.15 0.01 23843 0.812 3-fold ( 1 1 1) {+l,+h,+k} {+k,+l,+h} 12 0.055 0.11 0.01 24859 0.825 3-fold ( 1-1-1) {-l,-h,+k} {-k,+l,-h} 13 0.055 0.14 0.01 22467 0.788 3-fold ( 1-1 1) {+l,-h,-k} {-k,-l,+h} 14 0.055 0.12 0.01 27122 0.817 3-fold ( 1 1-1) {-l,+h,-k} {+k,-l,-h} 15 0.061 -0.10 -0.01 25905 0.726 4-fold h ( 1 0 0) {+h,-l,+k} {+h,+l,-k} 16 0.060 2.53 0.25 23689 0.449 4-fold k ( 0 1 0) {+l,+k,-h} {-l,+k,+h} 17 0.049 0.56 0.06 25549 0.653 4-fold l ( 0 0 1) {-k,+h,+l} {+k,-h,+l}
... symmetry is actually orthorhombic (P 21 21 21)
Laue Group Lklhd NetZc Zc+ Zc- CC CC- Rmeas R- Delta ReindexOperator= 1 P m m m *** 0.989 8.93 9.59 0.66 0.96 0.07 0.12 0.69 0.0 [-h,-l,-k] 2 P 1 2/m 1 0.003 7.85 9.65 1.80 0.97 0.18 0.09 0.60 0.0 [-h,-l,-k] 3 P 1 2/m 1 0.003 7.95 9.63 1.68 0.96 0.17 0.10 0.61 0.0 [l,h,k] 4 P 1 2/m 1 0.003 7.80 9.61 1.81 0.96 0.18 0.11 0.60 0.0 [h,k,l] 5 P 4/m m m 0.000 6.69 6.90 0.21 0.69 0.02 0.24 0.75 1.5 [-k,-h,-l] 6 P 4/m m m 0.000 4.55 5.41 0.85 0.54 0.09 0.34 0.68 0.1 [-l,-k,-h] 7 P 4/m 0.000 5.45 7.20 1.75 0.72 0.18 0.20 0.62 1.5 [-k,-h,-l] 8 P 4/m 0.000 4.72 6.53 1.81 0.65 0.18 0.25 0.60 0.1 [-l,-k,-h] 9 P -1 0.000 7.48 9.70 2.22 0.97 0.22 0.07 0.57 0.0 [-h,-l,-k] 10 P 4/m 0.000 4.03 5.96 1.92 0.60 0.19 0.29 0.59 1.4 [-h,-l,-k] 11 P 4/m m m 0.000 4.93 5.63 0.69 0.56 0.07 0.32 0.69 1.4 [-h,-l,-k] 12 C m m m 0.000 4.97 6.67 1.70 0.67 0.17 0.24 0.62 1.5 [h-k,-h-k,-l] 13 C 1 2/m 1 0.000 4.80 6.99 2.19 0.70 0.22 0.21 0.57 1.5 [-h-k,-h+k,-l] 14 C 1 2/m 1 0.000 4.51 6.71 2.20 0.67 0.22 0.23 0.58 1.5 [h-k,-h-k,-l] 15 C m m m 0.000 3.08 5.01 1.93 0.50 0.19 0.36 0.59 0.1 [-k-l,-k+l,-h] 16 P m -3 0.000 3.35 4.32 0.97 0.43 0.10 0.44 0.63 1.5 [h,k,l] 17 C 1 2/m 1 0.000 2.58 4.95 2.36 0.49 0.24 0.35 0.56 0.1 [k-l,-k-l,-h] 18 C 1 2/m 1 0.000 2.65 5.01 2.36 0.50 0.24 0.34 0.56 0.1 [-k-l,-k+l,-h] 19 H -3 0.000 2.17 4.56 2.39 0.46 0.24 0.40 0.55 1.5 [-k+l,-h-l,h-k-l] 20 H -3 0.000 2.09 4.48 2.39 0.45 0.24 0.40 0.55 1.5 [h-l,-h-k,-h+k-l] 21 H -3 0.000 2.15 4.54 2.39 0.45 0.24 0.39 0.55 1.5 [-h+k,-k-l,-h-k+l] 22 H -3 0.000 2.20 4.59 2.38 0.46 0.24 0.39 0.55 1.5 [k-l,h-k,-h-k-l] 23 C 1 2/m 1 0.000 3.10 5.42 2.32 0.54 0.23 0.31 0.56 1.4 [-h-l,h-l,-k] 24 C 1 2/m 1 0.000 3.36 5.67 2.31 0.57 0.23 0.30 0.56 1.4 [-h+l,-h-l,-k] 25 C m m m 0.000 3.32 5.29 1.97 0.53 0.20 0.34 0.59 1.4 [-h-l,h-l,-k] 26 H -3 m 0.000 -0.01 2.66 2.67 0.27 0.27 0.52 0.54 1.5 [-h+k,-k-l,-h-k+l] 27 H -3 m 0.000 -0.03 2.65 2.68 0.26 0.27 0.52 0.54 1.5 [k-l,h-k,-h-k-l] 28 H -3 m 0.000 -0.13 2.58 2.71 0.26 0.27 0.53 0.53 1.5 [h-l,-h-k,-h+k-l] 29 H -3 m 0.000 -0.02 2.66 2.68 0.27 0.27 0.52 0.53 1.5 [-k+l,-h-l,h-k-l] 30 P m -3 m 0.000 2.67 2.67 0.00 0.27 0.00 0.53 0.00 1.5 [h,k,l]

## Slide 16
Combining multiple files (and multiple MAD datasets)
Dataset 1, pk, 3 files
Dataset 2, ip, 1 file
Dataset 3, rm, 1 file
3 files assigned to same dataset
Because of an indexing ambiguity (pseudo-cubic orthorhombic), we must check for consistent indexing between files

## Slide 17: Alternative indexing
If the true point group is lower symmetry than the lattice group, alternative valid but non-equivalent indexing schemes are possible, related by symmetry operators present in lattice group but not in point group (note that these are also the cases where merohedral twinning is possible)
eg if in space group P3 (or P31) there are 4 different schemes (h,k,l) or (-h,-k,l) or (k,h,-l) or (-k,-h,-l)
For the first crystal, you can choose any scheme
For subsequent crystals, the autoindexing will randomly choose one setting, and we need to make it consistent: POINTLESS will do this for you by comparing the unmerged test data to a reference dataset (merged or unmerged)
Space group from HKLIN file : R 3 :H Cell: 257.89 257.89 144.72 90.00 90.00 120.00Alternative index test relative to reference file Alternative reindexing CC R(E^2) Number Cell_deviation [h,k,l] 0.885 0.157 6537 0.81 [k,h,-l] -0.001 0.511 6084 0.81

## Slide 18
Unit cell 74.72 129.22 184.25 90 90 90
This has b ≈ √3 a so can also be indexed on a hexagonal lattice,
lattice point group P622 (P6/mmm), with the reindex operator: h/2+k/2, h/2-k/2, -l
Conversely, a hexagonal lattice may be indexed as C222 in three distinct ways, so there is a 2 in 3 chance of the indexing program choosing the wrong one
A confusing case in C222:
Hexagonal axes (black)
Three alternative
C-centred orthorhombic
Lattices (coloured)

## Slide 19
Score each symmetry operator in P622
Only the orthorhombic symmetry operators are present
Correlation coefficient on E2
Rfactor (multiplicity weighted)
Nelmt Lklhd Z-cc CC N Rmeas Symmetry & operator (in Lattice Cell)
1 0.808 5.94 0.89 9313 0.115 identity
2 0.828 6.05 0.91 14088 0.141 *** 2-fold l ( 0 0 1) {-h,-k,+l}
3 0.000 0.06 0.01 16864 0.527 2-fold ( 1-1 0) {-k,-h,-l}
4 0.871 6.33 0.95 10418 0.100 *** 2-fold ( 2-1 0) {+h,-h-k,-l}
5 0.000 0.53 0.08 12639 0.559 2-fold h ( 1 0 0) {+h+k,-k,-l}
6 0.000 0.06 0.01 16015 0.562 2-fold ( 1 1 0) {+k,+h,-l}
7 0.870 6.32 0.95 2187 0.087 *** 2-fold k ( 0 1 0) {-h,+h+k,-l}
8 0.000 0.55 0.08 7552 0.540 2-fold (-1 2 0) {-h-k,+k,-l}
9 0.000 -0.12 -0.02 11978 0.598 3-fold l ( 0 0 1) {-h-k,+h,+l} {+k,-h-k,+l}
10 0.000 -0.06 -0.01 17036 0.582 6-fold l ( 0 0 1) {-k,+h+k,+l} {+h+k,-h,+l}
Z-score(CC)
“Likelihood”

## Slide 20
Scaling and Data Quality

## Slide 21
Determine point-group
(& space group)
and consistent indexing
Intensities
from Mosflm (or XDS)
h k l I σ(I) etc
POINTLESS
Sorted Intensities in “best” space group
AIMLESS/SCALA
Scale symmetry-related intensities together
Produce statistics on data quality
Estimate |F| from I
detect twinning (intensity statistics)
Complete sphere of reflections
Generate or copy freeR flags
Scaled and averaged intensities
CTRUNCATE
UNIQUIFY etc
h k l F σ(F) I σ(I) FreeR_flag
Data flow scheme in CCP4
Intensities
from Mosflm (or XDS)
h k l I σ(I) etc
Intensities
from Mosflm (or XDS)
h k l I σ(I) etc
One or more files from integration program
One or more datasets (eg MAD)
These programs may ultimately be combined into one
Note that this does not work well for very large numbers of crystals

## Slide 22: Choices
What scaling model?
  the scaling model should reflect the experiment
  considerations of scaling may affect design of experiment
Is the dataset any good?
  should it be thrown away immediately?
  what is the real resolution?
  are there bits which should be discarded (bad images)?

## Slide 23: Why are reflections on different scales?
Various physical factors lead to observed intensities being on different scales. Some corrections are known eg Lorentz and polarisation corrections, but others can only be determined from the data
Scaling models should if possible parameterise the experiment so different experiments may require different models
Understanding the effect of these factors allows a sensible design of correction and an understanding of what can go wrong
(a) Factors related to incident beam and the camera
(b) Factors related to the crystal and the diffracted beam
(c) Factors related to the detector

## Slide 24
(a) incident beam intensity: variable on synchrotrons and not normally measured. Assumed to be constant during a single image, or at least varying smoothly and slowly (relative to exposure time). If this is not true, the data will be poor
(b) illuminated volume: changes with φ if beam smaller than crystal
(c) absorption in primary beam by crystal: indistinguishable from (b)
(d) variations in rotation speed and shutter synchronisation. These errors are disastrous, difficult to detect, and (almost) impossible to correct for: we assume that the crystal rotation rate is constant and that adjacent images exactly abut in φ. (Shutter synchronisation errors lead to partial bias which may be positive, unlike the usual negative bias)
Data collection with open shutter (eg with Pilatus detector) avoids synchronisation errors (though variation in rotation speed could still cause trouble, and there is a dead time during readout)
Factors related to incident Xray beam

## Slide 25
(e) Absorption in secondary beam - serious at long wavelength (including CuKα)
(f) radiation damage - serious on high brilliance sources. Not easily correctable unless small as the structure is changing
Maybe extrapolate back to zero time? (but this needs high multiplicity)
The relative B-factor is largely a correction for the average radiation damage
Factors related to crystal and diffracted beam

## Slide 26
• The detector should be properly calibrated for spatial distortion and sensitivity of response, and should be stable. Problems with this are difficult to detect from diffraction data. There are known problems in the tile corners of CCD detectors (corrected for in XDS)
• The useful area of the detector should be calibrated or told to the integration program
– Calibration should flag defective pixels (hot or cold) and dead regions eg between tiles
– The user should tell the integration program about shadows from the beamstop, beamstop support or cryocooler (define bad areas by circles, rectangles, arcs etc)
Factors related to the detector

## Slide 27
Scaling
Scaling tries to make symmetry-related and duplicate measurements of a reflection equal, by modelling the diffraction experiment, principally as a function of the incident and diffracted beam directions in the crystal. This makes the data internally consistent.
Minimize Φ = Σhl whl (Ihl - 1/khl<Ih>)2
Ihl l’th intensity observation of reflection h
khl scale factor for Ihl <Ih> current estimate of Ih
ghl = 1/khl is a function of the parameters of the scaling model
ghl = g(φ rotation/image number) . g(time) . g(s) ...other factors
Primary beam s0 B-factor Absorption
Note that we do not know the true intensities and an internally-consistent dataset is not necessarily correct. Systematic errors which are the same for symmetry-related reflections will remain

## Slide 28
AIMLESS
Performs the same function as SCALA (only better of course!)
Read file from eg POINTLESS, sort data if necessary (SORTMTZ no longer needed)
Initial scale estimates from average intensities
First round scaling with small selection of strong reflections, chosen on I/σ(I)
First outlier rejection
Optimise the combination of profile-fitted (for weak spots) or summation integration intensities (for strong spots) from MOSFLM
First optimisation of σ(I) estimates
Main scaling on relatively strong reflections, chosen on normalised intensity E2
(eg 0.8 < E2 < 5)
Second outlier rejection
Final optimisation of σ(I) estimates
Final outlier rejection
Final statistics
Output of merged or unmerged data (MTZ or Scalepack format, or both)

## Slide 29
How can we measure data quality?
After scaling, the remaining differences between symmetry-related observations can be analysed to give an indication of data quality, though not necessarily of its absolute correctness.
We can also compare the intensities with their estimated errors to get signal/noise ratio
A. Measures of statistical significance:
I/σ(I) after averaging symmetry-related observations and after “correcting” σ(I) estimates (“Mn(I/sd)” in AIMLESS and SCALA output) is a measure of signal/noise
– but is sensitive to problems in the estimate of σ(I)

## Slide 30
B. Measures of internal consistency:
1. R-factors
  Rmerge = Σ | Ihl - <Ih> | / Σ | <Ih> | a.k.a Rsym or Rint
  traditional overall measures of quality, but increases with multiplicity although the data improves
Rmeas = Rr.i.m.= Σ √(n/n-1) | Ihl - <Ih> | / Σ | <Ih> |
    multiplicity-weighted, better (but larger)
Rp.i.m.= Σ √(1/n-1) | Ihl - <Ih> | / Σ | <Ih> |
    “Precision-indicating R-factor” gets better (smaller) with increasing multiplicity, ie it estimates the precision of the merged <I>
2. correlation coefficients
Half-dataset correlation coefficient:
Split observations for each reflection data randomly into 2 halves, and calculate the correlation coefficient between them
As a general rule , R-factors are good for measuring the difference between things that agree well, while correlation coefficients are better for measuring things which agree poorly

## Slide 31
Directions of analyses: analyses against “batch” (image number or “time”)
check for level of radiation damage
if you cut back from the end, there is a trade-off between damage and completeness
check for bad images or regions
A good case
No great difference between average scale Mn(k) & scale at θ=0
Small variation in relative B-factor
Uniform and low Rmerge
-0.8
0.0
0.04
0.06
0.0
0.02

## Slide 32
Increasing difference between average scale Mn(k) & scale at θ=0
relative B gets more negative with radiation damage
A bad case: two crystals, both dying, both incomplete
The relative B-factor gives a resolution-dependent scale factor as a function of “time” (dose): average radiation damage decay is greater at high resolution
k(time) = exp[-2B(time) sin2θ/λ2]
High and increasing Rmerge
-10
-5
0
0.1
0.2
0.3
“Resolution limit” where I/σ falls below 1.0 getting worse
Acceptable limit depends on resolution: B < -10 is bad!
Cumulative completeness
still very incomplete!

## Slide 33
Graph of Rmerge vs batch may also detect individual bad images, or bad regions, that should be investigated or rejected
One bad (weak) image
Bad region where integration had gone wrong
Omitting bad image
Reprocessed

## Slide 34
Analyses against intensity
Rmerge vs. I not generally useful (since R is a fractional measure, it will always be large for small I), but the value in the top intensity bin should be small
0.028
Improved estimate of σ(I)
Corrected σ’(Ihl)2 = SDfac2 [σ2 + SdB <Ih> + (SdAdd <Ih>)2]
The error estimate σ(I) from the integration program is too small particularly for large intensities. A “corrected” value may be estimated by increasing it for large intensities such that the mean scatter of scaled observations on average equals σ’(I), in all intensity ranges
SDfac, SdB and SdAdd are adjustable parameters
Should be = 1.0

## Slide 35
Directions of analyses: resolution
We can plot various statistics against resolution to determine where we should cut the data, allowing for anisotropy.
What do we mean by the “resolution” of the data? We want to determine the point at which adding another shell of data does not add any “significant” information, but how do we measure this?
Resolution is a contentious issue, often with referees, eg:
“The crystallographic Rmerge and Rmeas values are not acceptable, although, surprisingly the I/sigmaI and R-factors for these shells are OK. I cannot ever recall seeing such high values of Rmerge - 148% ! The discrepancy between the poor Rmerge values and vs. the other statistics is highly unusual- generally a high Rmerge corresponds a low I/sigma-I would have expected a value closer to 1.0 than 2.0 here - and no explanation is offered. The authors may want to decrease the claimed resolution such that acceptable values are obtained for all metrics.”
What scores can we use?
“The crystallographic structure determination is reported to be at 2.7Å resolution. However, the data statistics presented in table S1 show <I>/<<sigma>> =1.2 in the highest resolution shell and thus represent marginally significant reliability. Consequently, the resolution may be overstated.”

## Slide 36
What about R-factors?
Resolution
Rmerge
or Rmeas
high
1/d2
low
Where is the cut-off point?
Note that Rmerge
and Rmeas are useful for other purposes, but not for deciding the resolution cutoff
Note that the crystallographic R-factor behaves quite differently: at higher resolution as the data become noisier, Rcryst tends to a constant value, not to infinity

## Slide 37
What about I/σ(I) (signal/noise)?
Resolution
high
1/d2
low
1
2
3
20
40
I/σ(I)
after averaging
before averaging
Cut resolution at I/σ(I) after averaging (Mn(I/sd) = 2 (or maybe 1?)
A reasonably good criterion, but it relies on σ(I), which is not entirely reliable
Cut here?
?OK

## Slide 38
What about correlation coefficients?
Half-dataset correlation coefficient:
Split observations for each reflection randomly into 2 halves, and calculate the correlation coefficient between them
1.0
0.5
0
Resolution
Advantages:
Clear meaning to values (1.0 is perfect, 0 is no correlation) , known statistical properties
Independent of σ(I)
Maybe cut data at CC ~= 0.5
OK good

## Slide 39
Anisotropy
Many (perhaps most) datasets are anisotropic
The principal directions of anisotropy are defined by symmetry (axes or planes), except in the monoclinic and triclinic systems, in which we can calculate the orthogonal principle directions
We can then analyse half-dataset CCs or I/σ(I) in cones around the principle axes, or as projections on to the axes
Cones
Projections
I/σ(I) in cones
1.91Å
2.15Å
2.00Å
Anisotropic cutoffs are probably a Bad Thing, since it leads to strange series termination errors and problem with intensity statistics
So where should we cut the data?
Maybe at some compromise point

## Slide 40
How should we decide the resolution of a dataset?
I don’t know, but ...
“Best” resolution is different for different purposes, so don’t cut it too soon
Experimental phasing
substructure location is generally unweighted, so cut back conservatively to data with high signal/noise ratio
for phasing, use all “reasonable” data
Molecular replacement: Phaser uses likelihood weighting, but there is probably no gain in using the very weak high resolution data
Model building and refinement: if everything is perfectly weighted (perfect error models!), then extending the data should do no harm and may do good
There is no reason to suppose that cutting back the resolution to satisfy referees will improve your model!
Future developments may improve treatment of weak noisy data

## Slide 41
3.0Å
2.4Å
2.0Å
1.8Å
Rfree 0.294
Rfree 0.282
Rfree 0.285
Rfree 0.290
2.2Å
Rfree 0.284
figures made with ccp4mg
Example:
3 molecules/asu, omit 22/276 residues from each molecule, model build with Arp/warp at different resolutions
Number of residues built and sequenced
Cones
1.91Å
2.15Å
2.00Å
2.00Å
R & Rfree after initial refinement
Conclusion: there is not a huge difference

## Slide 42
Example continued: refinement against real data or simulated data
Rfree
Actual data (F)
Expected <F>
Random F around expected value
2.0Å
2.0Å
Half-dataset
CC(Iobs)
CC(Iobs v. calc)
~42%
~58%
Anisotropy
Thick lines:
Half-dataset CC(Iobs)
Thin lines:
CC(Iobs v. calc)
thanks to Garib Murshudov
All these indicators are roughly consistent that a suitable resolution cutoff is around 2.0Å, but that anything between 1.9Å and 2.1Å can be justified, with current technologies

## Slide 43
Reasons for outliers
• outside reliable area of detector (eg behind shadow)
specify backstop shadow, calibrate detector
• ice spots
do not get ice on your crystal!
• multiple lattices
find single crystal
• zingers
• bad prediction (spot not there)
improve prediction
• spot overlap
lower mosaicity, smaller slice, move detector back
deconvolute overlaps
Rejects lie on ice rings (red)
(ROGUEPLOT in Scala)
Position of rejects on detector
Outliers
Detection of outliers is easiest if the multiplicity is high
Removal of spots behind the backstop shadow does not work well at present: usually it rejects all the good ones, so tell Mosflm where the backstop shadow is.

## Slide 44
Detecting anomalous signals
The data contains both I+ (hkl) and I- (-h-k-l) observations and we can detect whether there is a significant difference between them.
Split one dataset randomly into two halves, calculate correlation between the two halves or
compare different wavelengths (MAD)
Plot ΔI1 against ΔI2
should be elongated along diagonal
Ratio of width of distribution along diagonal to width across diagonal
“RMS correlation ratio”
Correlation coefficient vs. resolution
Slope > 1.0 means that ΔI > σ
Strong anomalous signal
Ratio of width of distribution along diagonal to width across diagonal
Plot ΔI1 against ΔI2
should be elongated along diagonal
“RMS correlation ratio”
Correlation coefficient vs. resolution
Slope > 1.0 means that ΔI > σ
Weak but useful anomalous signal

## Slide 45
Intensities from Mosflm
h k l I σ(I) etc
Determine point-group
(& space group)
POINTLESS
Sorted Intensities in “best” space group
SCALA/AIMLESS
Scale symmetry-related intensities together
Produce statistics on data quality
Scaled and averaged intensities
CTRUNCATE
Estimate |F| from I
detect twinning (intensity statistics)
UNIQUIFY etc
Complete sphere of reflections
Generate or copy freeR flags
h k l F σ(F) I σ(I) FreeR_flag

## Slide 46
Estimation of amplitude |F| from intensity I
If we knew the true intensity J then we could just take the square root
        |F| = √J
But measured intensities I have an error σ(I) so a small intensity may be measured as negative.
The “best” estimate of |F| larger than √I for small intensities (<~ 3 σ(I)) to allow for the fact that we know than |F| must be positive
[c]truncate estimates |F| from I and σ(I) using the average intensity in the same resolution range: this give the prior probability p(J)
French & Wilson 1978

## Slide 47
Intensity statistics
We need to look at the distribution of intensities to detect twinning
Assuming atoms are randomly placed in the unit cell, then
<I>(s) = <F F*>(s) = Σj g(j, s)2
where g(j, s) is the scattering from atom j at s = sinθ/λ
Average intensity falls off with resolution, mainly because of atomic motions (B-factors)
<I>(s) = C exp (-2 B s2)
Wilson plot: log(<I>(s)) vs s2
This would be a straight line if all the atoms had the same B-factor
For the purposes of looking for crystal pathologies, we are not interested in the variation with resolution, so we can use “normalised” intensities which are independent of resolution

## Slide 48
Normalised intensities: relative to average intensity at that resolution
Z(h) = I(h)/<I(s)> ≈ |E|2
<Z(s)> = 1.0 by definition
<Z2(s)> >1.0 depending on the distribution
<Z2(s)> is larger if the distribution of intensities is wider: it is the 2nd moment ie the variance (this is the 4th moment of E)
many weak reflections
few weak reflections
Cumulative distribution of Z: p(Z) vs. Z
Z
1
0
0
p(Z)
many weak reflections
few weak reflections
p(Z1) is the proportion of reflections with Z < Z1
Z1
p(Z1)

## Slide 49
Other features of the intensity distribution which may obscure or mimic twinning
Translational non-crystallographic symmetry:
whole classes of reflections may be weak
eg h odd with a NCS translation of ~1/2, 0 0
<I> over all reflections is misleading, so Z values are inappropriate
The reflection classes should be separated (not yet done)
Anisotropy: <I> is misleading so Z values are wrong
ctruncate applies an anisotropic scaling before analysis
Overlapping spots: a strong reflection can inflate the value of a weak neighbour, leading to too few weak reflections
this mimics the effect of twinning

## Slide 50
Summary: Questions & Decisions
Do look critically at the data processing statistics
What is the point group (Laue group)?
What is the space group?
Was the crystal dead at the end?
Is the dataset complete?
Do you want to cut back the resolution?
Is this the best dataset so far for this project?
Should you merge data from multiple crystals?
Is there anomalous signal (if you expect one)?
Are the data twinned?
To help these developments, it would be useful to:
Deposit data to higher resolution than you might use
Deposit intensities as well as F
Deposit unmerged data (is this possible?)
Maybe deposit images?
Future developments may improve extraction of extra information from weak data at the resolution edge

## Slide 51
  Andrew Leslie many discussions
    Harry Powell many discussions
  Ralf Grosse-Kunstleve cctbx
    Kevin Cowtan clipper, C++ advice
Martyn Winn & CCP4 gang ccp4 libraries
Peter Briggs ccp4i
Airlie McCoy C++ advice, code etc
    Randy Read & co. minimiser
Graeme Winter testing & bug finding
Clemens Vonrhein testing & bug finding
Eleanor Dodson many discussions
Andrey Lebedev intensity statistics & twinning
Norman Stein ctruncate
Charles Ballard ctruncate
George Sheldrick discussions on symmetry detection
Acknowledgements